## Slide 1
TEAM 3
Julio Garcia
Philip Wahl
Jonas Mendoza
Nick Sheldon
Shayli Elrod
Hengrui Ju
ELECTRIC FEED
SYSTEM
FLIGHT-READY
ELECTRIC FEED SYSTEM

## Slide 2: AGENDA
Project Proposal
Customer/Engineering Requirements
Progress on Design
Gantt Chart
Ongoing Projects
Technical Writing Tips
Recap
ELECTRIC FEED SYSTEM

## Slide 3: PSAS has requested an Electric Feed System to pump two liquid propellants into the engine of their upcoming Launch Vehicle 4 to participate in the Base11 space challenge.
PROPOSAL
Sponsor: Portland State Aerospace Society
Project Title: Flight-Ready Electric Feed System
ELECTRIC FEED SYSTEM

## Slide 4
REQUIREMENTS
CUSTOMER | 
REQUIREMENT | Priority
Must be tested with LN2 and IPA | 5
Must safely keep the propellants separated at all times | 5
Should have embedded sensors for data collection | 5
Should have emergency shut off procedure and battery cutoff | 5
Control system should use sensor data | 4
Input pressure 45-100 PSI, Output pressure 450 PSI. | 4
Must be compatible with liquid oxygen (LOX) | 3
ELECTRIC FEED SYSTEM

## Slide 5
REQUIREMENTS
ENGINEERING |  |  | 
REQUIREMENTS | UNIT | ORIGINAL VALUE | UPDATED VALUE
PRESSURE | PSI | 400 | 450
MASS FLOW | lbm/s | 2.04 | 2.04
TOTAL SHAFT POWER | kW | 5.00 | 5.00
IPA ROTATIONAL SPEED | RPM | 20k | 35.6k
LN2 ROTATIONAL SPEED | RPM | 15k | 24.4k
ENGINE THRUST | kN | 2.2 | 2.2
MODULE DIAMETER | in | 12 | 12
ELECTRIC FEED SYSTEM

## Slide 6
ELECTRIC FEED SYSTEM
6061 Aluminum Prototype
Single Piece Design
CNC Lathe & CNC Mill
Final Iteration Coming Soon
IMPELLER MACHINING
PROGRESS ON DESIGN

## Slide 7
PROGRESS ON DESIGN
IPA Pump: Final Design
ELECTRIC FEED SYSTEM

## Slide 8
PROGRESS ON DESIGN
IPA Pump: Final Design
ELECTRIC FEED SYSTEM
0.008in
Combined impeller shaft design required z-axis restriction
Axially split collar solves issue with simple assembly
Safety measure to protect impeller face from impact in case of failure

## Slide 9
PROGRESS ON DESIGN
IPA Pump: Final Design
ELECTRIC FEED SYSTEM
Flowserve 0.5” ID Pac-Seal
Timken Tapered Roller Bearing

## Slide 10
ELECTRIC FEED SYSTEM
TP POWER BLDC MOTOR
SWORDFISH ESC
REVLECTRIX LiPO BATTERIES
SHAFT POWER COMPONENTS
PROGRESS ON DESIGN

## Slide 11
TEST STAND
MOBILE STATION
STEEL CONSTRUCTION
DUAL PUMP COMPATIBLE
FUEL TANK
STEEL TANK
½” NPT CONNECTIONS
125 PSI MAX PRESSURE
ELECTRIC FEED SYSTEM
PROGRESS ON DESIGN

## Slide 12
ELECTRIC FEED SYSTEM
EFS Gantt Chart
Today

## Slide 13
Ongoing Projects
ELECTRIC FEED SYSTEM
IPA CASE FINAL MANUFACTURING
Case_2 component. OP1 done, OP2 (backside – chamber ) toolpath ready.
Full case to be completed by 04/19/2019

## Slide 14
Full Scale IPA Pump Testing
ELECTRIC FEED SYSTEM
Ongoing Projects
TARGET DATE
04/23/2019
GOALS
Determine peak pressure and flowrate performance
Record manual throttle position for autonomous feedback operation
Identify weakness in design for continual improvement in functionality

## Slide 15
Ongoing Projects
Cryogenic Pump Design Considerations: Seal Selection
ELECTRIC FEED SYSTEM
C-Ring PTFE (Teflon) Energized
Spring Seal
Garlock PS-Seal (PTFE)
Marco Spring Energized Double
Coil Seal
For shaft seal . . .

## Slide 16
Ongoing Projects
Cryogenic Pump Design Considerations: Seal Selection
ELECTRIC FEED SYSTEM
For pump chamber . . .
PTFE (Teflon) sheets between chamber cases
Must be replaced semi-often
Will only be used if leak found

## Slide 17
Ongoing Projects
Cryogenic Pump Design Considerations: Case Material Selection
ELECTRIC FEED SYSTEM
Aluminum alloy will be used for Cryogenic (NO2) case
  Acceptable impact strength at low temps
  Low cost
  Easy to machine
  Options: 6061, 5038-O, 7075
  Different material may be required for LOX

## Slide 18
Ongoing Projects
Cryogenic Pump Design Considerations: Simulations
ELECTRIC FEED SYSTEM
FEA: Radial Impeller Deformation
CFD: Pump Chamber Pressure
Both works in progress
Shown promising results so far

## Slide 19
TECHNICAL WRITING
FEEDBACK
DESCRIPTIVE FIGURE CAPTIONS
SCALE COMPONENT IMAGES
LABEL PARTS IN DRAWINGS
DISCUSS RISK FACTORS ASSOCIATED WITH COMPONENTS
ELECTRIC FEED SYSTEM

## Slide 20
CONCLUSION
Creating Electric Feed System for PSAS
Full Scale IPA Pump Testing this Month
Cryogenic Pump Design being Finalized
ELECTRIC FEED SYSTEM